## Slide 1: THE IP NETWORK CONFLICT PROBLEM
Internal WiFi Card in NUC
Static IP Address: 192.168.1.1
Static IP Subnet Mask: 255.255.255.0
WiFi Network: 192.168.1.0/24
Intel NUC / IoT Gateway
VENUE ROUTER
Developer
Laptop
On Venue Ethernet
Venue Router / Network
Venue Network: 192.168.1.0/24
Venue Network Plugged into NUC Ethernet Jack
On Venue Network: 192.168.1.0/24
Venue Network Plugged into Laptop
On Venue Network: 192.168.1.0/24
The static IP Address assigned to the NUC’s WiFi Adapter is: 192.168.1.1
From that address, the NUC infers that the WiFi network it is hosting is:
192.168.1.0/24
If the NUC is plugged into your venue network, your venue’s network also is defined as:
192.168.1.0/24
The NUC get’s confused because it’s Ethernet and WiFi networks conflict.

## Slide 2
Internal WiFi Card in NUC
Static IP Address: 192.168.101.1
Static IP Subnet Mask: 255.255.255.0
WiFi Network IP: 192.168.101.0/24
Intel NUC / IoT Gateway
VENUE ROUTER
Developer
Laptop
On Venue Ethernet
Venue Router / Network
Venue Network: 192.168.1.0/24
Venue Network Plugged into NUC Ethernet Jack
On Venue Network: 192.168.1.0/24
Venue Network Plugged into Laptop
On Venue Network: 192.168.1.0/24
Change the Static IP of the NUC’s WiFi adapter so that it is on a different network. For example, changing the IP Address to:
192.168.101.1
With a subnet mask of
255.255.255.0
Puts it on the network:
192.168.101.0/24
The NUC will no longer be confused if it’s Ethernet port is plugged into a venue network of:
192.168.1.0/24
Note, you don’t have to use the 192.168.101.1 IP Address for your NUC’s wifi. Just make sure to use an IP Address / Subnet Mask combo for the WiFI adapter that puts it on a completely different network than the venue network.
THE IP NETWORK CONFLICT SOLUTION

## Slide 3
Intel NUC / IoT Gateway
VENUE ROUTER
Developer
Laptop
On Venue Ethernet
THE IP NETWORK CONFLICT EASY FIX
Connect an HDMI Monitor and Keyboard / Mouse directly to the NUC, then boot the NUC up.
Login as:
User Name: root
Password: root
Get the current IP Address used by the WiFi adapter by looking at the current network config:
cat /etc/config/network
br-lan Link encap:Ethernet HWaddr f0:42:1c:e1:29:31
inet addr:192.168.1.1 Bcast:192.168.1.255 Mask:255.255.255.0
inet6 addr: fe80::f242:1cff:fee1:2931/64 Scope:Link
UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
RX packets:455 errors:0 dropped:0 overruns:0 frame:0
TX packets:438 errors:0 dropped:0 overruns:0 carrier:0
collisions:0 txqueuelen:0
RX bytes:49098 (47.9 KiB) TX bytes:90109 (87.9 KiB)
Use sed to change the ip address from the old one to the new desired one in the /etc/config/network file
sudo sed –i ‘s/192.168.1.1/192.168.101.1/g’ /etc/config/network
Reboot the NUC:
shutdown –r 0